## Slide 1: EENG 385 Amplifier Theory
Notes: Usually the <title of the lab> is what will be called the “System” through the rest of this document

## Slide 2: Lab Objectives
The objective of this lab is to analyze the operation and electrical characteristics of the audio amplifier stage of the Audio board and to prepare you to solder together the audio amplifier subsystem of the Audio board.

## Slide 3: Theory
Two stage
Input from audio source via 3.5mm jack
Common emitter, voltage amplifier
Emitter follower, current amplifier
Notes: Replace <System> with the name of the

## Slide 4: Theory
Model circuit with small signal model
Vs is audio source, your MP3 player
Use analysis to determine values in colored boxes
Notes: Replace <System> with the name of the

## Slide 5: Small Signal Input Resistance
Small signal input resistance
  Looks at changes in voltage/current
Example: Find Rice
  V = I*R so Rice = ΔvB / ΔiB
  Effect of ΔvB on ΔvE at T4?
  Effect of ΔiE on ΔvE at T4?
  Relationship between ΔiB on ΔiE

## Slide 6: Assemble
Audio input & amplifier
Polarized parts
  100uF
  TIP 122 NPN
  TIP 127 PNP
  2N3904
  1k and 100k Pot
Notes: Replace <System> with the name of the

## Slide 7: Test
No testing of assembled circuit
  If POTs are not adjusted, it may look like your circuit has a short circuit
  Wait until next week’s lab to power up.
Notes: Replace <System> with the name of the

## Slide 8: Turn In
Audio Amplifier Steps 1 – 3
Common Emitter Theory Steps 1 – 3
The Vbe Multiplier Steps 1 – 12
Rice Steps 1 – 6
Roce Steps 1 – 2
Ace Steps 1 – 8
Rief Steps 1 – 6
Roef Steps 1 – 2
Aef Steps 1 – 2
Gain of amplifier with no load Steps 1 – 4
Gain of amplifier with 8Ω load Steps 1 – 4
Complete Table 1
Notes: Replace <System> with the name of the