## Slide 1: EENG 385 Filter Design: Assembly through Test
Notes: Usually the <title of the lab> is what will be called the “System” through the rest of this document

## Slide 2: Taking Lab Assistant Applications
The EENG 385 lab assistant position pays 4-hours a week. Responsibilities of a lab assistant include:
Attending a 4-hour EE Lab Assistant training event at the start of the term,
Working with another undergraduate lab assistant to run the lab. This includes helping students:
  Troubleshoot circuits,
  Interpreting lab instructions,
  Configuring test and measurement equipment
  Working with the software
Introducing the lab at the start of the class,
Grading the weekly lab deliverables and entering the grades in Canvas,
Spending 30 minutes reviewing the lab materials,
Meeting 30 minutes a week with the course instructor to review the lab.
This is a great way to both learn the materials and develop teamwork, leadership
and communication skills.

## Slide 3: Lab Objectives
The objective of this lab is to study the design, simulation and construction of the filters on the audio board and measure their performance.

## Slide 4: Theory
Audio Board has 3 filters
LPF and HPF are Sallen Key architecture
BPF is hybrid
Notes: Replace <System> with the name of the

## Slide 5: Theory
Sine wave input produces sine wave output
Frequency is preserved
Amplitude and Phase change
Notes: Replace <System> with the name of the

## Slide 6: Lab Content
Using the Audio Board Interface
Use the Analog Devices Wizard
Simulation: LTspice Time Domain
Simulation: LTspice Frequency Sweep
Circuit: Time Domain
Circuit: Frequency Response Analysis
Notes: Replace <System> with the name of the

## Slide 7: Using the Audio Board Interface
Each filter is connected to an input and output header.
Labeled on the PCB
Daisy chain signals
  Connect Signal input to LEVELin
  Connect LEVELout to LPFin
  Connect LPFout to audio header

## Slide 8: How to: Analog Devices Wizard
Specify filter performance, use RC slider to get decade caps!
Get filter topology and component values. Use E6 resistors!
Notes: Replace <System> with the name of the

## Slide 9: How to: LTspice Point-by-point
Build model in LTspice
Apply sin wave at some frequency
Measure change in amplitude in dB
Measure change in phase in degrees
Plot dB and phase as a function of frequency
Notes: Replace <System> with the name of the

## Slide 10: How to: LTspice Frequency Sweep
Build model in LTspice
Use AC Analysis tool
Plot dB and phase as a function of frequency
Notes: Replace <System> with the name of the

## Slide 11: How to: Circuit Point-by-Point
Assemble filter on Audio board
Apply sin wave at some frequency
Measure change in amplitude in dB
Measure change in phase in degrees
Plot dB and phase as a function of frequency
Notes: Replace <System> with the name of the

## Slide 12: How to: Circuit Frequency Sweep
Configure Audio board
  Function gen into level shifter
  Level shift out to filter in
Configure oscilloscope probes
  Ch 1 = filter input
  Ch 2 = filter output
Use oscilloscope FRA function
Scope plots mag and phase as a function of frequency
Notes: Replace <System> with the name of the

## Slide 13: Assemble
Use Wizard to
  Meet design requirements
  Determine topology – should match PCB
  Determine component values
    Use E6 resistors 100, 150, 220, 330, 470, 680
    Use E1 capacitors 1nF, 10nF, 100nF, 1uF, etc…
  If needed,
    Put components in parallel to create needed values
Notes: Replace <System> with the name of the

## Slide 14: Turn In
Level Shifter
  Analysis
Low Pass Filter
  Design using Wizard
  Simulation analysis using point-by-point and FRA
  Assemble and test using point-by-point and FRA
High Pass and Band Pass Filter
  Design using Wizard
  Assemble and test using FRA