## Slide 1: Oscilloscope Basics
Mines Maker Society
and Mines IEEE

## Slide 2: Oscilloscope Parts
Touchscreen
Softkeys
USB Port
Controls
Ch. 1 vertical controls
Ch. 2 vertical controls
Probe connectors
Horizontal controls

## Slide 3: Oscilloscope Probe
Probe
(Connect to the part of the circuit you want to test.)
Ground Clip
(Connect to the ground reference of your circuit. This is also connected to earth ground through the oscilloscope.)

## Slide 4: Setting Attenuation
There are 3 kinds of probes available in our labs
10x attenuation with pin,
No need to set manually
10x attenuation without pin,
Need to set manually
1x/10x attenuation without pin,
Need to set manually and match to the switch on the probe

## Slide 5: Setting Attenuation
Press here
Click “Attenuation” and set to proper value
Proper value should be shown

## Slide 6: Oscilloscope Trigger
The trigger determines where it aligns your time cursor

## Slide 7: Oscilloscope Trigger
You can also set the direction for the trigger (rising or falling)
Rising
Falling

## Slide 8: Cursors
You can take manual voltage and time measurements using the cursors

## Slide 9: Measurements
The oscope can also make many standard measurements for you

## Slide 10: Measurements
Top left: Phase
Top right: Amplitude
Bottom left: Peak-to-peak
Bottom Right: Percent overshoot

## Slide 11: Acquire
If you have a noisy signal, you can average a number of captures to isolate the signal you want to see