## Slide 1: EENG 385 Full Bridge Rectifier with Buck Converter
Notes: Usually the <title of the lab> is what will be called the “System” through the rest of this document

## Slide 2: Lab Objectives
Study the theory, simulation and implementation of a full-bridge rectifier and a switch mode DC-to-DC converter.

## Slide 3: Power Conversion PCB
Bridge Rectifier – Converts 17VAC into 17VDC
Buck Converter – Steps 17VDC down using PWM duty cycle
Notes: Replace <System> with the name of the

## Slide 4: Full Bridge Rectifier
AC input Vac+/Vac- DC output Vrec+/GND
Diodes “correct” negative voltages, making them positive
Capacitor stores charges for when AC voltage dips low
Adjustable load S1
Probe points
Notes: Replace <System> with the name of the

## Slide 5: Full Bridge Rectifier
Input:
Output:
Small resistor +
Smaller capacitor =
Larger ripple
Notes: Replace <System> with the name of the

## Slide 6: Mains Step-down transformer
KS21239L4 Transformer
Input 120VAC 3-prong plug
Output 4 screw-terminals
Voltage measured RMS
Notes: Replace <System> with the name of the

## Slide 7: Full Bridge Rectifier
Implementation
  VAC from transformer
  Oscilloscope to Vrec+
Notes: Replace <System> with the name of the

## Slide 8: Buck Converter
V_REC+ from Bridge Rectifier
PWM duty cycle
V_BUCK is step down output
MOSFET Q2/Q3 are switches
Q2 Enables PWM to switch Q3
Q3 Closed charges L1/C2
Q3 Open discharges L1/C2

## Slide 9: Buck Converter
Simulation
Adjust duty cycle and load
Record Vout DC (average)
Record Vout ripple

## Slide 10: Buck Converter
Implementation
Adjust duty cycle and load
Record Vout DC (average)
Record Vout ripple

## Slide 11: Turn In
Make a record of your response to numbered items below
Full Bridge Rectifier Theory
Steps 1 – 8
Full Bridge Rectifier Simulation
Table 1
Full Bridge Rectifier Implementation
Steps 1-7
Table 1
Oscilloscope trace with 100Ω and 470Ω load
Buck Converter Theory
PWM High Steps 1-5
PWM Low Steps 1-4
Buck Converter Simulation
Steps 1-6
Table 3
Buck Converter Implementation
Steps 1-4
Complete Table 4
Relationships 1-4