## Slide 1: EENG 385 BJT Curve Tracer Calibration
Notes: Usually the <title of the lab> is what will be called the “System” through the rest of this document

## Slide 2: Lab Objectives
Objective: Finish assembly of BJT Curve Tracer and use it to measure the gain and Early voltage of three BJTs.

## Slide 3: Theory
Device Under Test = DUT
Draw family of characteristic curves on oscilloscope
Provide vce and ib as inputs then measure ic as the output
Notes: Replace <System> with the name of the

## Slide 4: Theory
Imagine oscilloscope drawing an image using a beam
  Oscilloscopes used CRTs
X-position of beam
  Controlled by voltage on Ch1
Y-position of beam
  Controlled by voltage on Ch2
Can create complex images
  IC vs. VCE family of curves
Notes: Replace <System> with the name of the

## Slide 5: Analyze
Ramp - 0.7V is applied to collector of DUT
Current mirror converts Ic into voltage across 100Ω
VSTAIR is converted to base current through 100kΩ
  You will measure the voltage of each step convert to base current
  You can do this before soldering in components
Step | VSTAIR(V) | ib (uA)
6 | 7.6 | 15
5 | 6.4 | 12
4 | 5.1 | 9.4
3 | 3.9 | 6.8
2 | 2.6 | 4.0
1 | 1.4 | 1.5
0 | 0V | 0
Notes: Replace <System> with the name of the

## Slide 6: Assemble
Two 2N3906 PNP in 385 parts bin
One 2N7000 NMOS in 385 parts bin
Misc. resistors and 3-pin DUT socket in parts bin
Use resistor leads for GND, CH_X and CH_Y loops
Notes: Replace <System> with the name of the

## Slide 7: Matching transistors
Current mirror
  Circled in red
  Works perfectly when beta are same
Choose
  Same font = same lot
  Use DCA75 Pro measure Beta
Notes: Replace <System> with the name of the

## Slide 8: Test
Different BJTs will have different pinouts
Will not harm DUT BJT if you put it in backwards
Check datasheet for pinout
Use jumper wires as needed
Notes: Replace <System> with the name of the

## Slide 9: Test
Base current
Measure Vic at Vce = 1V
Use cursors for Early voltage
Notes: Replace <System> with the name of the

## Slide 10: Turn In
This is an individual assignment – turn in your performance cards
You can work in teams of two during this lab
Fill out 3 BJT Performance Cards for:
  2N2222 (in 385 parts bin)
  2N3904 (in 385 parts bin)
  BD139 (in 385 parts bin)
  !!!RETURN WHEN DONE!!!
Save BJT card as PDF
Due before start of class next week
Every student uses their own board
Everyone brings their board to class