## Slide 1: Electronic Devices and Circuits Lab 03 – ramp generator
Lab overview
Objective: The objective of this lab is analyze, simulate and assemble the pseudo ramp generator.

## Slide 2: Pseudo ramp generator
The 10nF capacitor C3 charges towards VCC = 9V
  Charges for 270us then reset (by 555 timer)
  The charging is close to a straight line
Compare charging cap to a straight line in Excel
Chart: Cap Charging vs. Time
| 0 | 1.0000000000000001E-5 | 2.0000000000000002E-5 | 3.0000000000000004E-5 | 4.0000000000000003E-5 | 5.0000000000000002E-5 | 6.0000000000000002E-5 | 7.0000000000000007E-5 | 8.0000000000000007E-5 | 9.0000000000000006E-5 | 1E-4 | 1.1E-4 | 1.2E-4 | 1.3000000000000002E-4 | 1.4000000000000001E-4 | 1.5000000000000001E-4 | 1.6000000000000001E-4 | 1.7000000000000001E-4 | 1.8000000000000001E-4 | 1.9000000000000001E-4 | 2.0000000000000001E-4 | 2.1000000000000001E-4 | 2.2000000000000001E-4 | 2.3000000000000001E-4 | 2.4000000000000001E-4 | 2.5000000000000001E-4 | 2.6000000000000003E-4 | 2.7000000000000006E-4 | 2.8000000000000008E-4
Ramp | 0 | 0.080325 | 0.16065 | 0.24097 | 0.3213 | 0.40162 | 0.48195 | 0.56227 | 0.6426 | 0.72292 | 0.80325 | 0.88357 | 0.9639 | 1.0442 | 1.1245 | 1.2049 | 1.2852 | 1.3655 | 1.4458 | 1.5262 | 1.6065 | 1.6868 | 1.7671 | 1.8475 | 1.9278 | 2.0081 | 2.0884 | 2.1688 | 2.2491
Charge | 0 | 0.089551 | 0.17821 | 0.26599 | 0.3529 | 0.43894 | 0.52412 | 0.60846 | 0.69195 | 0.77462 | 0.85646 | 0.93749 | 1.0177 | 1.0971 | 1.1758 | 1.2536 | 1.3307 | 1.407 | 1.4826 | 1.5574 | 1.6314 | 1.7047 | 1.7773 | 1.8492 | 1.9203 | 1.9908 | 2.0605 | 2.1296 | 2.1979

## Slide 3: Simulation
Build in Multisim
  Charge on capacitor is cleared by MOSFET
  Do not include Schmitt Trigger Oscillator in simulation
Simulate to verify calculations

## Slide 4: Assemble
Assemble
  Annoying big 100k
  2N7000 clears charge off cap

## Slide 5: Test
Probe 555TIMER (yellow) and RAMP (blue)
RAMP is bottom terminal of
unoccupied R21 resistor

## Slide 6: Turn in
Summary of analysis, simulation and assemble
Answer listed questions
Save solutions as PDF
Due before start of class next week
Every student builds their own board
Everyone brings their board to class