## Slide 1: EENG 385 Audio Board Power Supply
Notes: Usually the <title of the lab> is what will be called the “System” through the rest of this document

## Slide 2: Lab Objectives
The objective of this lab is to study the components and design of a power supply including linear regulators, Zener diodes and reverse voltage protections and start you on the path to constructing the Audio board.

## Slide 3: Power Supply Subsystem
Schematic Layout

## Slide 4: 7805 Linear Regulator
Input voltage = 5V + dropout voltage
Output voltage = 5V
Dissipates excess voltage as heat P = ΔV * I
  ΔV =Vin – 5V
  I is current to load
Pmax around 1Watt
Notes: Replace <System> with the name of the

## Slide 5: Zener Diode - 1N4733
Reverse biased
  Clamps to 5.1V
  Used to limit or regulate voltage
Forward biased
  Clamps to 1.2V
Notes: Replace <System> with the name of the

## Slide 6: Zener Diode - 1N5222
Reverse biased
  Clamps to 2.5V
  Used to regulate voltage
Notes: Replace <System> with the name of the

## Slide 7: P-channel MOSFET - FQP27P06
Vg < Vs
  Short circuit between S and D
Vg > Vs
  Open circuit between S and D
Notes: Replace <System> with the name of the

## Slide 8: LED
The power-on LED provides positive confirmation that power is bring delivered to the circuit.
This is a “must-add” to any PCB you are designing
Notes: Replace <System> with the name of the

## Slide 9: Theory
Reverse Voltage Protection
FQP27P06 acts like a switch
  Open when Vsg < 3V
  Closed when Vsg > 3V
1N4733 Zener diode
  Limits Vsg of MOSFET to 5.1V
  Forward biased Vgs =1.2V
Notes: Replace <System> with the name of the

## Slide 10: Turn In
Make a record of your response to numbered items below
LM7805 Questions 1 – 5
Zener Diode Questions 1 – 3
Power-on LED Questions 1 – 9
On/off switch Questions 1 – 2
Reverse Volt Questions 1-7
Solder only the power supply subsystem
Do not solder audio and filter components
Test voltage outputs with DMM
Sign your name on your PCB