## Slide 1
1
EENG385 - Electronic Devices and Circuits
Lab 07:
Audio Amplifier Analysis
Objective:
    Study the design and of the audio board.
    Create amplifier model

## Slide 2: Overall structure
2
2
Two stage
Input from audio source via 3.5mm jack
Input stage if common emitter, voltage amplifier
Output stage is common collector, current amplifier.
Notes: 2

## Slide 3: Mathematical Model
3
3
Source is your MP3 player
Use analysis to determine values
Lots of simple math
Notes: 3

## Slide 4: Working with Audio Amplifier
4
4
You will need
  Speaker (don’t get to keep)
  Audio cable (don’t get to keep)
Power at 9V with lab supply
Supply audio through cable
Install jumper wire
  Audio input
  Amplifier input
Adjust bias of POT
  Circled in red
Watch for things getting hot
Notes: 4

## Slide 5: Measure performance
5
5
Measure no speaker
  Voltage from MP3 player (yellow)
  Collector of first stage BJT (blue)
  Relative amplitudes are what matters
Notes: 5

## Slide 6: Measure performance
6
6
Measure with speaker
  Voltage from MP3 player (yellow)
  Collector of first stage BJT (blue)
  Relative amplitudes are what matters
Different ratio
Notes: 6

## Slide 7: Have fun
7
7
Components are safe up to 25V or so
Find a big speakers – give it a go!
Decrease emitter resistor for more gain
Things may get hot
  I have heat sinks if needed
  Use FLIR camera to keep an eye on things
  Lick finger before touching suspect component
    Sizzle = hot
    Smell for melting components
Notes: 7