## Slide 1: EENG 385 Amplifier Measurements
Notes: Usually the <title of the lab> is what will be called the “System” through the rest of this document

## Slide 2: Lab Objectives
The objective of this lab is to configure, use, and analyze the audio amplifier on the Audio board and compare the results to the analysis performed last week.

## Slide 3: Setup Step 1 - initialization
Vbe Multiplier POT (left one)
  Turn CW at least 20 turns. You may hear it click.
Vbias POT (right one)
  Turn CCW at least 20 turns. You may hear it click it click.
  Turn CW 4 turns
Install jumper
Configure oscilloscope
Connect 3.5mm audio cable to source
Connect Power Supply with 16V and 0.2A
Load YouTube
Notes: Replace <System> with the name of the

## Slide 4: Setup Step 2 - Vbias
Adjust Vbias POT CW/CCW
Center waveforms to 8V
Notes: Replace <System> with the name of the

## Slide 5: Setup Step 3 - Vbe
Adjust Vbe POT CCW
Separate waves by 2.4V
Just before current spikes
Notes: Replace <System> with the name of the

## Slide 6: Setup Step 4 - Vbias
Adjust Vbias POT CW/CCW
Re-center waveforms to 8V
Notes: Replace <System> with the name of the

## Slide 7: Test No Speaker Gain
Measure no speaker
Voltage from MP3 player (yellow)
Collector of first stage BJT (blue)
Relative amplitudes are what matters
Notes: Replace <System> with the name of the

## Slide 8: Test With Speaker Gain
Measure with speaker
Voltage from MP3 player (yellow)
Collector of first stage BJT (blue)
Relative amplitudes are what matters
Notes: Replace <System> with the name of the

## Slide 9: Bode Plot Pro Tip
Use BNC T-connector to send oscilloscope function output to
  Oscilloscope Channel 1 using BNC to BNC cable
  Circuit using function generator cable
T-connector BNC to BNC cable Function Gen Cable

## Slide 10: Turn In
Amplifier Measurements
  Screen shot of input and output with no-load
  Calculation of no-load gain
  Screen shot of input and output with 8Ω speaker
  Calculation of 8Ω gain.
  Bode plot of amplifier
Apply an Audio Source
  Demo working amplifier by playing a song
Notes: Replace <System> with the name of the

## Slide 11: Have Fun
Components are safe up to 25V or so
Find a big speakers – give it a go!
Decrease emitter resistor for more gain
Things may get hot
  Adjust Vbe POT as needed
  I have heat sinks if needed
  Use FLIR camera to keep an eye on things
  Lick finger before touching suspect component Sizzle = hot
  Smell for melting components