## Slide 1: EENG 385 Total Harmonic Distortion
Notes: Usually the <title of the lab> is what will be called the “System” through the rest of this document

## Slide 2: Taking Lab Assistant Applications
The EENG 385 lab assistant position pays 4-hours a week. Responsibilities of a lab assistant include:
Attending a 4-hour EE Lab Assistant training event at the start of the term,
Working with another undergraduate lab assistant to run the lab. This includes helping students:
  Troubleshoot circuits,
  Interpreting lab instructions,
  Configuring test and measurement equipment
  Working with the software
Introducing the lab at the start of the class,
Grading the weekly lab deliverables and entering the grades in Canvas,
Spending 30 minutes reviewing the lab materials,
Meeting 30 minutes a week with the course instructor to review the lab.
This is a great way to both learn the materials and develop teamwork, leadership
and communication skills. There are some other perks that I am working on, so stand by.

## Slide 3: Lab Objectives
The objective of this lab is to measure the total harmonic distortion (THD) of the audio amplifier using the FFT feature of the oscilloscope.

## Slide 4: Theory
Fundamental
  Frequency of input
Harmonics
  Integer multiple of fundamental
Oscope FFT
  X axis is frequency
  Y axis is power @ frequency
Perfect amplifier
  All power in fundamental
Notes: Replace <System> with the name of the

## Slide 5: Theory
Total Harmonic Distortion
Decibels relative to carrier (dBc) measured on oscilloscope
Collect dBc values from harmonics
Perform math in Excel
Notes: Replace <System> with the name of the

## Slide 6: Test
Setup Time Domain
Freq Domain
Notes: Replace <System> with the name of the

## Slide 7: Test
Search function automates FFT measurement
Noise floor = average lowest
Threshold = absolute
Excursion = relative to floor
Peaks = Threshold OR Excursion
Tips
  Use Averaged Value improve noise floor
  Use Run/Stop
Notes: Replace <System> with the name of the

## Slide 8: Turn In
Table 1
Complete THD graph
  X axis = Vpp
  Y axis = THD
  For several frequencies
Chart: 
| 0.2 | 0.5 | 1
220 | 0.0070879 | 0.010248 | 0.014014
470 | 0.0090411 | 0.01291 | 0.089042
1kHz | 0.095041 | 0.15251 | 0.23483
2.2k | 0.0029478 | 0.012558 | 0.15566
4.7k | 0.0089125 | 0.016438 | 0.20101